## Slide 1
1
DrainFlow
Storm Sewer Design Assistant
CE 206 : Engineering Computation Sessional | MATLAB Project
GROUP 01
Section- B2
2304099
Amartya Halder
2304104
Md. Fahmidul Haq
2304109
Md. Jubayer Hasan
2304114
Beprojit Das Dipto
2304119
Md. Kawser Ahmed Rakib
2304124
Nur Afra
2304129
Muhammad Sheikh Akbar Kabir
Notes: Title slide. State project name, group number and that this is the final presentation. ~20 seconds.

## Slide 2
2
Objectives
Why Urban Storm Sewers Need Better Preliminary Design?
Preliminary sewer design today is largely manual: repeated hand calculation for every trial pipe size and rainfall scenario.
Engineers need a fast, repeatable way to estimate peak runoff and check whether a proposed pipe can safely carry it — before detailed design begins.
Objective: Build an interactive MATLAB app that estimates peak runoff (Rational Method), sizes and verifies storm sewer pipes (Manning's Equation), and visualizes hydraulic performance in real time.
Notes: Read these quickly - they map one-to-one onto the calculation slides later. ~30 seconds.

## Slide 3
3
Problem Statement
Urban stormwater must be carried away safely. A storm sewer fails in four distinct ways:
Insufficient capacity
Excessive velocity
Insufficient velocity
Oversized design
The design engineer must therefore answer two coupled questions:
How much water arrives? Rainfall → runoff → required discharge Q
Can the pipe carry it? Diameter, slope, roughness → capacity, depth, velocity
Notes: Frame the four failure modes early - the design checks later map onto exactly these. ~45 seconds.

## Slide 4
4
Methodology
Program logic, from catchment inputs to design decision
HYDROLOGY
Catchment & pipe inputs
Time of concentration
Kirpich
Design rainfall intensity
IDF interpolation
Required discharge
Rational Method
HYDRAULICS
Full-pipe capacity
Manning
Partially full geometry
circular segment
Bisection method
root of Q(y) − Q_req = 0
Normal depth y and velocity V
DECISION
Capacity check
Q_full vs Q_req
Velocity checks
0.6 – 3.0 m/s
Pipe sizing sweep
smallest adequate D
DESIGN STATUS
OK / WARN / FAIL
Notes: Walk the three phases left to right. Emphasise that bisection is the computational core. ~60 seconds.

## Slide 5
6
Governing Equations
Manning's equation
Q_Capacity = (1/n) · A · R²ᐟ³ · S¹ᐟ²
V = Q / A
A flow cross-sectional area (m²)
R hydraulic radius A/P (m)
S pipe slope (m/m)
n Manning roughness coefficient
P wetted perimeter — wall only
Peak runoff (Rational Method)
Q_Req = C · i · A / 360
Q peak discharge (m³/s) ·
C runoff coefficient ·
i intensity (mm/hr) ·
A catchment area (ha) ·
360 unit conversion
Notes: The note about the free surface matters - it is the reason Q peaks before the pipe is full. ~40 seconds.

## Slide 6
5
Additional Equations
Time of concentration (Kirpich)
tᴄ = 0.0195 · L⁰·⁷⁷ · Sᴄ⁻⁰·³⁸⁵
tᴄ time of concentration (min) · L overland flow length (m) · Sᴄ catchment slope (m/m)
Design rainfall intensity (log–log interpolation)
ln i = ln i₁ + f · ( ln i₂ − ln i₁ ) , f = ln(t/t₁) / ln(t₂/t₁)
i intensity (mm/hr) · t duration (min) · i₁, i₂ tabulated values · f position in log-duration space
Partially full circular pipe
θ = 2 · cos⁻¹ ( 1 − 2y/D )
A = (D²/8) · ( θ − sin θ )
P = Dθ / 2
R = A / P
θ, P, A, R are Partially Fully Circular Pipe Dimensions
Notes: Do not derive anything here - just name each equation and its role. ~35 seconds.

## Slide 7
5
Partially full circular pipe
θ = 2 · cos⁻¹ ( 1 − 2y/D )
A = (D²/8) · ( θ − sin θ )
P = Dθ / 2
R = A / P
θ, P, A, R are Partially Fully Circular Pipe Dimensions
Notes: Do not derive anything here - just name each equation and its role. ~35 seconds.

## Slide 8
7
Assumptions
Rational Method for peak runoff
Valid for small urban catchments; rainfall uniform over the area
Storm duration = time of concentration
The whole catchment contributes simultaneously at this duration
Triangular rainfall pattern
Used for the live visualisation only, not for the design calculation
Manning's equation for pipe flow
Steady, uniform flow; normal depth assumed to be established
Circular pipe cross-section
Flow area treated as a circular segment
Normal depth obtained numerically
The depth equation cannot be rearranged algebraically
Velocity limits 0.6 – 3.0 m/s
Self-cleansing at the lower end, scour protection at the upper
Capacity judged on full-bore flow
The part-full discharge bonus is deliberately not claimed
Notes: These are the assumptions actually coded, not a generic textbook list. ~40 seconds.

## Slide 9
8
Program Structure
How the functions call one another
DrainFlow (main GUI)
recompute() — runs on every input change
time_of_concentration
idf_intensity
rational_Q
manning_capacity
solveDepth
bisect_root
manning_Q
pipe_geometry
Animation and reporting branch
triangular_hyetograph
drawHero · drawHydro · drawBar
printReport · runoff_volume · pipe_sizing
manning_capacity also calls manning_Q. printReport re-runs every calculation at tight tolerance and prints the full audit trail.
Notes: No source code shown, per the instructions - only the call relationships. ~45 seconds.

## Slide 10
9
Program Structure
Engineering functions
time_of_concentration
Kirpich travel time
IN L, Sc
OUT tc (minutes)
idf_intensity
Reads the Khulna IDF table
IN duration, return period
OUT i (mm/hr), exact-or-interpolated flag
rational_Q
Peak runoff
IN C, i, A
OUT Q (m³/s)
pipe_geometry
Circular-segment properties
IN y, D
OUT A, P, R, top width, θ
manning_Q
Forward Manning solution
IN y, D, S, n
OUT Q, V, R, A
Notes: Five core engineering functions. Each is independently testable. ~30 seconds.

## Slide 11
10
Program Structure
Numerical and support functions
manning_capacity
Full-bore and maximum discharge
IN D, S, n
OUT Qfull, Vfull, Qmax, y at Qmax
bisect_root
General bracketed root finder
IN f, xl, xu, tolerance, max iter
OUT root, f(root), error, iterations
solveDepth
Inverts Manning for depth
IN Q required, D, S, n
OUT normal depth y
triangular_hyetograph
Design storm shape
IN t, duration, peak intensity
OUT i(t) (vectorised)
runoff_volume
Trapezoidal and Simpson integration
IN hydrograph Q(t)
OUT storm runoff volume (m³)
pipe_sizing
Diameter sweep, 0.15 – 2.00 m
IN Q required, S, n
OUT smallest adequate D, commercial size
Notes: bisect_root is written as a general-purpose solver, not tied to this problem. ~30 seconds.

## Slide 12
11
Live Demonstration
The DrainFlow interface
DrainFlow — full interface
Catchment & rainfall
area, C, length, slope, return period
Pipe design
diameter, slope, material roughness
Live readouts
tᴄ, required Q, pipe capacity
Pipe animation
water depth solved every frame
Hyetograph & runoff
storm shape and discharge
Capacity vs demand
the design check, as bars
Notes: Switch to MATLAB here. Point at each region of the window as you name it. ~40 seconds.

## Slide 13
12
Live Demonstration — Design Passes
REQUIRED Q
0.6328
CAPACITY
0.7872
VELOCITY
1.98 m/s
STATUS
OK
DESIGN PASSES
CONDITION
Q_Capacity ≥ Q_req
0.6 ≤ V ≤ 3.0 m/s
Notes: Case 1 of 4. This is the input set every hand calculation that follows is based on. ~25 seconds.

## Slide 14
13
Live Demonstration — Undersized Pipe
REQUIRED Q
0.9505
CAPACITY
0.7872
VELOCITY
1.78 m/s
STATUS
FAIL
UNDERSIZED
CONDITION
Q_Capacity < Q_req
Notes: Case 2. Larger catchment, same pipe. Point out that the drawing goes solid red at y/D = 100 %. ~25 seconds.

## Slide 15
14
Live Demonstration — Velocity Too High
REQUIRED Q
0.6328
CAPACITY
1.3531
VELOCITY
3.01 m/s
STATUS
WARN
VELOCITY TOO HIGH
EROSION RISK
CONDITION
V > 3.0 m/s
Notes: Case 3. Steeper slope. Q rises as the square root of S, but so does velocity. ~25 seconds.

## Slide 16
15
Live Demonstration — Velocity Too Low
REQUIRED Q
0.1442
CAPACITY
1.2655
VELOCITY
0.56 m/s
STATUS
WARN
VELOCITY TOO LOW
SILTATION RISK
CONDITION
V < 0.6 m/s
Notes: Case 4. The important lesson: enlarging a pipe to fix capacity can create this problem. The criteria fight each other. ~30 seconds.

## Slide 17
16
Sample Calculation — Input Data
Every following slide uses this one input set
Catchment area
A
2.00
ha
Runoff coefficient
C
0.65
—
Overland flow length
L
600
m
Catchment slope
Sᴄ
0.0050
m/m
Return period
T
10
yr
Pipe diameter
D
0.75
m
Pipe slope
S
0.0050
m/m
Manning roughness
n
0.013
—
Storm duration is set equal to the time of concentration — concrete pipe, Khulna IDF table
Notes: Establish the sample. Say it matches the default state the program opens with. ~20 seconds.

## Slide 18
17
1
Time of Concentration
FORMULA
tᴄ = 0.0195 · L⁰·⁷⁷ · Sᴄ⁻⁰·³⁸⁵
SUBSTITUTION
tᴄ = 0.0195 × (600)⁰·⁷⁷ × (0.0050)⁻⁰·³⁸⁵
tᴄ = 0.0195 × 137.777 × 7.6895
RESULT
tᴄ = 20.66 min
MATLAB output — t_c = 20.7 min
NOMENCLATURE
tᴄ
time of concentration
min
L
overland flow length
m
Sᴄ
catchment slope
m/m
0.0195
Kirpich empirical constant, SI form
Notes: Kirpich. Longer path increases travel time, steeper slope reduces it. ~35 seconds.

## Slide 19
18
2
Design Rainfall Intensity
FORMULA
ln i = ln i₁ + f · ( ln i₂ − ln i₁ )
SUBSTITUTION
15 min → 218.15 mm/hr 30 min → 135.76 mm/hr
Since 15 < 20.66 < 30, interpolate in log–log space:
f = ln(20.66/15) / ln(30/15) = 0.4618
ln i = ln(218.15) + 0.4618 × [ ln(135.76) − ln(218.15) ]
RESULT
i = 175.24 mm/hr
Linear interpolation would give 187.1 mm/hr — 6.8 % high, because IDF curves are convex.
MATLAB output — i = 175.2 mm/hr
NOMENCLATURE
i
design rainfall intensity
mm/hr
i₁, i₂
tabulated intensities either side
mm/hr
t₁, t₂
bracketing table durations
min
f
position in log-duration space
—
T
return period
yr
Notes: Stress WHY log-log: IDF curves are power laws, straight on log axes. Linear interpolation cuts the corner. ~50 seconds.

## Slide 20
19
3
Required Discharge — Rational Method
FORMULA
Q = C · i · A / 360
SUBSTITUTION
Q = ( 0.65 × 175.24 × 2.00 ) / 360
Q = 227.81 / 360
RESULT
Q_req = 0.6328 m³/s
360 is a unit conversion, not an empirical constant: 1 mm/hr over 1 ha = 10/3600 m³/s.
MATLAB output — Required Q
NOMENCLATURE
Q
peak runoff discharge
m³/s
C
runoff coefficient
—
i
rainfall intensity
mm/hr
A
catchment area
ha
360
unit conversion factor
—
Notes: Be ready for the classic question: where does 360 come from? Derive it in one line. ~35 seconds.

## Slide 21
20
4
Full-Pipe Geometry
FORMULA
A = πD²/4 R = D/4
SUBSTITUTION
A = π × (0.75)² / 4 = 0.4418 m²
R = 0.75 / 4 = 0.1875 m
RESULT
A = 0.4418 m² R = 0.1875 m
NOMENCLATURE
A
full-bore flow area
m²
D
internal pipe diameter
m
P
wetted perimeter (= πD when full)
m
R
hydraulic radius, A / P
m
Notes: Quick slide. The R = D/4 result falls straight out of A/P. ~25 seconds.

## Slide 22
21
5
Full-Pipe Capacity — Manning
FORMULA
Q = (1/n) · A · R²ᐟ³ · S¹ᐟ²
SUBSTITUTION
Q = (1/0.013) × 0.4418 × (0.1875)²ᐟ³ × (0.0050)¹ᐟ²
Q = 76.923 × 0.4418 × 0.32759 × 0.070711
RESULT
Q_Cap = 0.7872 m³/s
MATLAB output — Pipe capacity
NOMENCLATURE
Q
full-bore discharge capacity
m³/s
n
Manning roughness coefficient
—
A
flow cross-sectional area
m²
R
hydraulic radius
m
S
pipe slope
m/m
V
mean flow velocity, Q / A
m/s
Notes: Accumulate the product left to right so each step can be checked against the report. ~35 seconds.

## Slide 23
22
6
Capacity Check
REQUIRED
0.6328
m³/s
CAPACITY
0.7872
m³/s
Capacity / demand = 0.7872 / 0.6328 = 1.244
Q_Capacity > Q_req
CAPACITY CHECK PASSES
MATLAB — Capacity vs peak demand
NOMENCLATURE
Q_req
required peak discharge
m³/s
Q_full
full-bore pipe capacity
m³/s
ratio
Q_full / Q_req, the spare margin
—
Notes: Capacity is tested first because it governs. 24 % spare here. ~30 seconds.

## Slide 24
23
7
Partially Full Pipe — the Inverse Problem
FORMULA
Q(y) = (1/n) · A(y) · R(y)²ᐟ³ · S¹ᐟ²
SUBSTITUTION
θ = 2 cos⁻¹ ( 1 − 2y/D ) A = (D²/8)(θ − sin θ)
P = Dθ / 2 R = A / P
Required: find y such that Q(y) = Q_req
RESULT
y cannot be isolated
y sits inside an arccos, inside a sine, inside a 5/3 power. The equation is transcendental — no algebraic rearrangement exists.
NOMENCLATURE
y
flow depth
m
θ
central angle of the wetted arc
rad
A(y)
flow area at depth y
m²
P(y)
wetted perimeter — wall only
m
R(y)
hydraulic radius, A / P
m
Q_req
discharge that must be carried
m³/s
Notes: This is the honest justification for a numerical method - not 'we were told to use one'. ~40 seconds.

## Slide 25
8
Bisection Method
ALGORITHM
1
Bracket the root: f(yₗ) < 0, f(yᵤ) > 0
2
Midpoint yₘ = ( yₗ + yᵤ ) / 2
3
Evaluate f(yₘ) = Q(yₘ) − Q_req
4
Keep the half that still brackets the root
5
Repeat until the relative error ≤ tolerance
yₗ , yᵤ lower and upper bracket depths (m) yₘ midpoint depth (m)
f(y) Q(y) − Q_req, the residual (m³/s) eₐ approximate relative error (%)
ITERATION TRACE
it
yₗ
yᵤ
yₘ
eₐ (%)
1
0.0000
0.7036
0.3518
100.00
2
0.3518
0.7036
0.5277
33.33
3
0.3518
0.5277
0.4398
20.00
4
0.4398
0.5277
0.4838
9.09
5
0.4838
0.5277
0.5057
4.35
6
0.5057
0.5277
0.5167
2.13
7
0.5057
0.5167
0.5112
1.08
⋮
21
0.5092
0.000066
Notes: Bisection chosen for guaranteed convergence - it runs 20 times a second inside the animation with nobody watching. ~55 seconds.

## Slide 26
25
9
Normal Depth
FORMULA
solve Q(y) = Q_req = 0.6328 m³/s
SUBSTITUTION
Bracket [ 0 , 0.9382 × 0.75 ] = [ 0 , 0.7036 ] m
21 bisection iterations, relative error 6.6 × 10⁻⁵ %
y / D = 0.5092 / 0.75
RESULT
y = 0.5092 m y/D = 67.9 %
Error bound after 21 halvings: 0.7036 / 2²¹ = 3.4 × 10⁻⁷ m.
NOMENCLATURE
y
Flow Depth
m
y/D
relative depth ratio
%
0.9382 D
depth of maximum discharge
m
eₐ
approximate relative error
%
Notes: Make the two numbers the visual focus. ~30 seconds.

## Slide 27
26
10
Flow Area at the Normal Depth
FORMULA
θ = 2 cos⁻¹(1 − 2y/D) A = (D²/8)(θ − sin θ)
SUBSTITUTION
θ = 2 cos⁻¹ ( 1 − 2×0.5092/0.75 ) = 3.8738 rad
A = (0.75²/8) × ( 3.8738 + 0.6628 ) = 0.3194 m²
P = 0.75 × 3.8738 / 2 = 1.4527 m
R = 0.3194 / 1.4527 = 0.2199 m
RESULT
Flow Area = 0.3194 m²
A/A_full = 72.3 % while y/D = 67.9 % — the pipe is fuller by area than by depth.
NOMENCLATURE
θ
central angle of the wetted arc
rad
A_flow
flow area at the normal depth
m²
P
wetted perimeter
m
R
hydraulic radius, A / P
m
D
internal pipe diameter
m
Notes: This is the area the velocity must be divided by - NOT the full-pipe area. ~35 seconds.

## Slide 28
27
11
Flow Velocity and Design Status
FORMULA → SUBSTITUTION
V = Q / Flow Area
V = 0.6328 / 0.3194
V = 1.9814 m/s
VELOCITY WINDOW
0.6 ≤ 1.9814 ≤ 3.0 m/s
OK — DESIGN PASSES
NOMENCLATURE
V
mean flow velocity
m/s
Q
discharge carried
m³/s
F.A.
flow area at the normal depth
m²
MATLAB status line
Notes: The GUI status line reads V = 1.98 m/s. If anyone asks about 1.43, that is Q divided by the full-pipe area - a common slip. ~40 seconds.

## Slide 29
28
Graph 1 — Hyetograph & Runoff Response
MATLAB — hyetograph and hydrograph, design-passes case
Blue curve
Rainfall intensity i(t) — mm/hr, left axis
Orange curve
Rational Method runoff Q(t) — m³/s, right axis
Dashed red line
Full-pipe capacity Q_full
Thin vertical line
Current simulation time
Shaded area
Area under i(t) = rainfall depth
Notes: If asked why the red capacity line sits exactly on the blue apex: both axes auto-scale to 1.15x their own maximum, so it is an axis-scaling coincidence, not a physical result. ~40 seconds.

## Slide 30
30
Graph 2 — Capacity vs Peak Demand
MATLAB — capacity vs peak demand
REQUIRED Q
0.6328 m³/s
PIPE CAPACITY
0.7872 m³/s
Capacity > Required
1.244
capacity / demand ratio
Notes: The capacity bar turns red automatically when the pipe is undersized. ~25 seconds.

## Slide 31
31
Graphical Pipe Response
MATLAB — pipe drawn at the instantaneous depth, late in the storm
Rainfall intensity i(t)
Q(t) = C · i(t) · A / 360
Manning: Q(y) − Q(t) = 0
Bisection every frame
Normal depth y(t)
Water level drawn to scale
Notes: Strongest single feature of the GUI - say explicitly that bisection runs every frame. ~30 seconds.

## Slide 32
32
Validation — MATLAB vs Hand Calculation
Same sample input set, computed independently by hand
PARAMETER
HAND CALCULATION
MATLAB
% ERROR
Time of concentration
20.659 min
20.659 min
0.00 %
Rainfall intensity
175.24 mm/hr
175.24 mm/hr
0.00 %
Required discharge
0.63281 m³/s
0.63281 m³/s
0.00 %
Full-pipe capacity
0.78721 m³/s
0.78721 m³/s
0.00 %
Full-pipe velocity
1.7819 m/s
1.7819 m/s
0.00 %
Normal depth
0.50924 m
0.50924 m
0.00 %
Flow velocity
1.9814 m/s
1.9814 m/s
0.00 %
Notes: Do not oversell this table - zero error is expected. The next slide is the real validation. ~35 seconds.

## Slide 33
34
CE 206 Topics Applied
MATLAB fundamentals
Vectorised operations, logical masking, input validation, structured program layout
User-defined functions
Every engineering calculation isolated in its own testable function
Roots of equations
Bisection applied to Q(y) − Q_req = 0; bracketing, convergence, tolerance
Curve fitting & interpolation
Log–log interpolation in duration; linear interpolation in the reduced variate
Numerical integration
Trapezoidal rule and Simpson's 1/3 rule for runoff volume
Plotting & visualisation
Dual-axis live plots, bar comparison, animated patch graphics
Not used in this project
Eigenvalues · Fourier analysis · Ordinary differential equations · Numerical differentiation
We claim only the topics the program genuinely uses.
Notes: Naming what was NOT used reads as honesty and usually pre-empts a question. ~30 seconds.

## Slide 34
35
Challenges & How We Resolved Them
CHALLENGE
HOW WE RESOLVED IT
Depth equation cannot be rearranged
Recast as a root problem and solved with bisection
Q(y) is not monotonic — two roots possible
Bracket capped at y = 0.9382 D, where Q(y) is strictly increasing
Circular-segment geometry repeated everywhere
Isolated in one pipe_geometry function returning A, P, R, θ
Solver too slow for a live animation
Loose tolerance for the 20 fps loop, tight tolerance for the printed report
IDF table too coarse for tᴄ = 20.66 min
Log–log interpolation in duration, reduced-variate interpolation in return period
Proving the results are right
Back-substitution residual plus an independent grid search
Notes: These are all post-progress-presentation problems, as the instructions ask. ~45 seconds.

## Slide 35
36
Current Limitations
No rainfall–runoff lag or routing
Rational Method applied instantaneously; hydrograph timing not modelled
Triangular storm is a visualisation shape
The Rational Method's implicit design storm is uniform, not triangular
Animated storm volume is not IDF-consistent
Triangle peak = IDF intensity, so its average is half. Peak discharge is unaffected
Kirpich is a rural formula, used uncorrected
Urban paved catchments normally take a correction factor of about 0.4
Runoff coefficient C is a judgement value
Q is linear in C; a ±0.1 swing moves the design flow by ±15 %
Stored Khulna IDF table only
Short durations were disaggregated from daily records, not gauged directly
Single pipe, no network
No manholes, junctions, backwater or surcharge analysis
No infiltration or catchment storage model
Losses are lumped entirely into the constant C
Numerical precision (10⁻⁷) far exceeds input accuracy (10⁻¹). Precision is not the same thing as accuracy.
Notes: Close on the precision-vs-accuracy line. It is the single best sentence in the deck. ~50 seconds.

## Slide 36
37
Future Work
A staged roadmap beyond this course
Extend to multi-pipe networks
Add manholes, junctions, surcharge
Automated report and drawing export
Notes: Keep this brisk - it is a roadmap, not a commitment. ~25 seconds.

## Slide 37
38
Conclusion & Learning Outcomes
SAMPLE DESIGN SUMMARY
Time of concentration
20.66 min
Rainfall intensity
175.24 mm/hr
Required discharge
0.6328 m³/s
Pipe capacity
0.7872 m³/s
Normal depth
0.5092 m
Depth ratio y/D
67.9 %
Flow velocity
1.9814 m/s
Pipe diameter
0.75 m
STATUS — DESIGN PASSES
Learning outcomes
Translating governing engineering equations into structured, testable MATLAB code
Recognising when a problem needs a numerical method — and being able to justify it
Choosing robustness over speed: bisection's guaranteed convergence beats Newton's rate here
Understanding why a pipe carries more flow when it is not quite full
Validating computational output against hand calculation and an independent method
Distinguishing numerical precision from engineering accuracy
Notes: Land the last learning outcome deliberately - precision is not accuracy. ~45 seconds.

## Slide 38
39
Thank You
Questions & Discussion
DrainFlow · Storm Sewer Design Assistant · CE 206
Notes: Likely questions: why bisection not Newton; where does 360 come from; why does Q peak before full; why no lag in the hydrograph.